PHYSICS

PAPER 3

232/3

MARKING SCHEME

1.	a)	f = 15 cm±2

b)

| Object distance (u cm) | 22 | 24 | 26 | 28 | 30 | 32 | 34 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Image distance (vcm) | 32.9 | 34.2 | 36.0 | 38.9 | 39.5 | 41.0 | 42.1 |
| Magnification |  |  |  |  |  |  |  |

-	For  u±0.2 cm values a ward 4 marks for all values within range. See accuracy above otherwise a ward ½ mark for each.

-	For m award 2 marks for all values correct but 4- 5 values correct a ward  1 mark and less than 4 values correct a ward 0 marks.

c)	Axes 1mk – both quantity and unit on V axis

Scale (1mk)	simple and uniform

Plotting (2mks)	atleast four correctly plotted points

Line (1mk)	- line passing through atleast three correctly points.

d)	Gradient/ slope =

PART B

ii)	E=1.5±01

iii)	V=1.4±0.1

iv)	I = 0.12±0.01A

E-V=Ir

0.1 = 0.12 x 8

R =

=	 0.83Ω

Question 2

PART A

a)	R = 600±10

On presence of plain paper showing how r is got

| Angle of incidence (Deg) | 30 | 35 | 40 | 45 | 50 | 55 | 60 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Angle (degree) | 14 | 22 | 34 | 39 | 43 | 48 | 51 |
| E = 90 - |  |  |  |  |  |  |  |

f)	Axes 1mk – must be labeled

scale 1mk) – simple and uniform

plotting (1mk) – atleast four correctly plotted points curve (1mk)- passing through 3 points and smooth.

ii)	i0 =470

PART B

a)	G = 50±0.5cm

b)	i)	P = 67.3±0.5cm

ii)	Y = 67.3 – 50

= 17.3 cm

iii)	Clockwise moments = Anti clockwise moments

(50x- 17.3)+u = (100x 10)

U= 1000-865

=135 N